## Slide 1: Importing Files to Komatsu IMC dozer

## Slide 2: Important Information
Files need to be located on the root folder of the thumb drive being used to load files – files cannot be in a folder
Project File Format - .tp3 (TIN, Linework, Localization)
Surface File Format - .tn3 (TIN file)
Linework File Format - .ln3 (Linework file)
Localization File Format - .gc3 (Control)

## Slide 3: Hit File Button and Select Projects

## Slide 4: Hit the Copy Button

## Slide 5: From: USB to 3DMC then highlight file you want to copy

## Slide 6: Select the New Project File – then hit OK

## Slide 7: Set an Active Surface

## Slide 8: Loading TIN (.tn3) File
If only the surface (finish grade) of the project changes, you can load a new .tn3 file.
This will keep all the other project information (linework, calibration, etc) the same
You will now be able to select the newly loaded surface as the active surface
The original surface file will remain part of the project file
.tn3 file needs to be on the root drive of a thumb drive

## Slide 9: Go to File and Select Surfaces

## Slide 10: Hit Import to Add New Surface File

## Slide 11: File must be stored in 3DMC folder

## Slide 12: Highlight Surface to Import

## Slide 13: Add New Surface to Current Project

## Slide 14: Set New Surface as Active Surface